Short answer problems [24 points]

Que1.
Given an example of how one can exploit the associative property of convolution to more efficiently filter an image.

Solution1.
Example: suppose there are two filters f,h and which has to be applied on an image g
In this case by the associative property of convolution we can write

        (f*g)*h = (f*h)*g
Both operation on LHS and RHS produces the same result but the computational complexity of the operations are different.

Computational Complexity:
       Suppose f → x*y matrix.
       Suppose h → x*y matrix.
       and g is an image matrix → X*Y matrix.

Then the computational complexity for RHS is
   O((x*y)*(x*y)) + O((x*y)*(X*Y))

And the computational complexity of LHS is
   2*O((x*y)*(X*Y)) i.e. 1st convolving image with filter then again convolving the output image obtained with another filter.

As the size of filters f,h are much smaller as compared to the image size so
Computation complexity of RHS is less as compared to that of LHS.

So RHS is considered as the most efficient way of convolution i.e. by convolving all filters first then convolve the image.

Que2.
This is the input image: [1 0 1 1 1 1 1 1]. What is the result of erosion with a structuring element [1 1 1]?

Solution2.
Output obtained after applying erosion:- [0 0 0 1 1 1 1 1]

Que3.
Describe a possible flaw in the use of additive Gaussian noise to represent image noise.

Solution3.
The noise in the real world images can be caused due to various factor like: wind,sand fire and also the orientation of the camera. So this is the reason why modeling of noise with Gaussian may not describe the real world applications.

Que4.
Design a method that takes video data from a camera perched above a conveyor belt at an automotive equipment manufacturer, and reports any flaws in the assembly of a part. Your response should be a list of concise, specific steps, and should incorporate several techniques covered in class thus far. Specify any important assumptions your method makes.
Solution4.